HAZARDOUS MATERIALS / HAZARDOUS WASTE /STORMWATER

Storage and Maintenance Area Self-Inspection Form

| Inspection Date | Area free of spills/leaks/litter/debris | Proper 2ndary containment | Containment clean | Container conditions sound | Containers labeled | Incompatibles segregated | Waste tagged and dated | Waste within storage time | Emergency procedures posted | Equipment outside stored properly | Check for non-stormwater discharge | Area free from erosion | Inspector’s initials | Comments / Corrective Actions |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Hazardous Materials and Hazardous Waste Storage Areas must be inspected at least monthly.

Hazardous Materials and Hazardous Waste Storage Areas must be inspected at least monthly.  Explain any problems found and corrective actions taken in the “Comments” section.  This log is part of the facility operating records and must be kept for a minimum of three (3) years.

How to Use the Storage Area Self-Inspection Form

This form may be used for self-inspections of hazardous material storage areas, hazardous waste accumulation areas and/or maintenance areas.

Area Inspected:

The area or areas being inspected should be indicated on the form. Each unit may decide how many forms are needed to best cover their storage and maintenance areas.

Inspection Date:

Enter the month, day and year of the self-inspection.

Area free of spills/leaks/litter/debris:

- Look on and around hazardous material containers and hazardous waste containers for signs of spilled or leaked materials. There should be no visible signs of contamination on tops or sides of waste containers, in the containment, or elsewhere in the general storage area. Wipe down or clean containers, containment and the storage area as necessary. Is there any trash or debris including sediment on the ground or in the storm drains.

Proper secondary containment:

- Is the secondary containment of adequate size? The volume of the secondary containment needs to be:

  - 110% the volume of a single container if only one is present or,

  - if multiple containers use a single secondary containment, the containment volume should be the larger of 150% of the largest container volume, or 10% of the total volume of all the containers.

- Is the secondary containment compatible with the chemicals to be stored? Make sure it won’t be degraded or corroded by a spill.

- Are all materials stored in the same secondary containment compatible? Make sure they won't chemically react with each other.

- The adequacy of secondary containment is dependent on many specifics of the storage location. If you would like assistance, contact hazwaste@ucsc.edu.

Container conditions sound:

- All containers of hazardous materials and hazardous wastes should be closed with a tightly fitting lid. A properly sealed container in sound condition will not leak when laid on its side or overturned.

Containers labeled:

- All containers, whether the contents are hazardous or non-hazardous, including individual use containers, squeeze bottles and spray bottles, should have a legible label, which at a minimum indicates the name of the product and the primary hazard of the contents.  Generally recognized products do not need the hazard indicated.

Incompatibles segregated:

- Are materials that could adversely interact with each other or the other containers separated by secondary containment and/or distance?  For instance, are acids kept away from bases and flammables/combustibles separated from oxidizers? The product SDS is a good source for identifying incompatible materials.

- For materials transferred to a new container, such as a spray bottle, is the material compatible with the new container?

Waste tagged and dated:

- As soon as even one drop of hazardous waste is first added to a container, the EH&S hazardous waste label must be completed and attached.

- Hazardous waste labels are printed on line via the WASTe system (ehs.ucop.edu/waste). For instructions, refer to http://ehs.ucsc.edu/programs/waste-management/documents/WazUserGuide.pdf

Waste within storage time:

  - For areas subject to satellite accumulation requirements (almost all campus waste storage areas), containers should be removed within 3 months. To conform to regulatory requirements, all containers must be designated for pickup through the WASTe program (ehs.ucop.edu/waste) within 6 months of the accumulation start date.

Emergency procedures:

- For each area where hazardous materials or wastes are stored, verify that simplified response guides for emergencies are posted.  Refer to http://ehs.ucsc.edu/programs/environmental/hazmat-storage.html

Equipment outside stored properly:

  - Are equipment and parts with oily components or other pollutant sources (e.g., metals) that must be stored outside under cover or covered with plastic sheeting or tarps to avoid contamination of storm water? Are tarps in good condition?

Check for Non-stormwater discharge:

  - Is there evidence of non-storm water discharges into the storm water system? Is there evidence of authorized non-storm water discharges? (e.g., from the eye wash station, fire system testing/flushing, or air conditioning condensate.)?

Area free from erosoin:

Is there evidence of erosion?  Are sediment and vegetative waste collected from cleaning activities?

Inspector’s initials

Comments/Corrective actions:

- Explain any problems found and corrective actions taken.  Follow-up promptly on deficiencies noted. When corrections are completed, initial, date and explain corrective actions taken.