Hazardous Waste

Satellite Accumulation Area

Post this sheet to designate hazardous waste accumulation area

Satellite Accumulation Areas (SAA)- Federal regulations (40 CFR 262.34(c)(1)) allow a generator to accumulate as much as 55 gallons of hazardous waste or one quart of acutely or extremely hazardous waste in containers at or near any point of generation.

TRAINING

- Before you generate waste you must attend a hazardous waste training course offered by EH&S or must be under direct supervision of a properly trained person.

LABELING REQUIREMENTS

- A waste container must be labeled with an Online Tag Program (OTP) label as soon as the first drop is added to the container.

- Each container must be labeled with the full name of the chemical components with a percentage equaling 100%.

- Do not use abbreviations or chemical notation.

- All waste should be disposed of within 6 months of accumulation start date.

STORAGE REQUIREMENTS

- Designate a single location for the storage of hazardous waste.

- The storage area must be under the control of the operator of the process generating the waste and the SAA must be at or near the point of generation.

- The waste must be compatible with the containers and lids.

- Fill waste containers to only 80% of capacity.

- The containers must be closed except during the adding or removing of waste.

- Incompatibles must be segregated.

- All waste containers must be in clean secondary containment.

- The containers must be free of exterior contamination.

- Waste containers must be stored in a safe location and easily accessible.

INSPECTIONS

- All waste storage areas are required to have a monthly documented inspection, certifying there are no leaks or spills and that the above labeling and storage requirements have been met.   Form available on the EH&S web site. http://ehs.ucsc.edu/programs/waste-management/hazmatwaste-form.doc

NOTES

- Do not evaporate solvent wastes in fume hood or open laboratory.

- Do not dispose of hazardous wastes in the sewer or ordinary trash.

- Fume hoods should not be used as designated waste storage areas.

- There are time and volume limitations on the generation of extremely hazardous (EH) wastes.  Refer to the waste management link on EH&S web site for more information.

- Any questions, contact Hazardous Waste Program Manager at 459-3086